## Slide 1: Let us begin
Hardik Shah
Robotics and Embedded Systems
Department of Informatics
Technische Universität München
www6.in.tum.de
29 October 2015

## Slide 2: Overview
Current state of the car
Application 1
Application 2
Application 3
Application 4
Application 5
Application 6

## Slide 3: Topic - 1
Driver development for the WiFi module and communication protocol with mobile App
  CC3000 WiFi module
  Driver code for Arduino available from Adafruit (port it)
  Decide on communication protocol
Begin with an Arduino and CC3000 module (provided)
  Try to get the Arduino communicate the world via “Edurom” or HotSpot-AP created by your mobile phone
  Study the code to point out “Hardware dependent functions”
    Finally, we will replace the Arduino by the DE0-nano board
    Start making a clean document about your findings

## Slide 4: Topic - 2
Vehicle management and control
  Receive commands from different “actors”
  Process commands according to current operation mode and priorities
  Manage uC OS-II for co-ordination activities
  Port DMP code for Gyro/Accel and Compass
  Periodically read sensor values and store in a data structure accessible by all actors
Begin with DE0 board and use “Hello uC” template for a new project using the .SOPCINFO file provided last week
  Create periodic tasks to read from the sensors (HC-SR04, MPU 6050, Compass (remember bypass?), wheel encoders)
  Build apps for driving the car
  Discuss with other teams about the way of communication

## Slide 5: Topic - 3
Autonomous parking
  As the name suggests!
  Identity parking slot using ultrasonic sensors
  Depending on the slot dimensions, plan your trajectory
  Sensors used: Ultrasonic, wheel encoders and compass
Begin with DE0 board and use “Hello uC” template for a new project using the .SOPCINFO file provided last week
  Yours is also a task which is scheduled periodically and quits immediately if parking is not requested
  Work closely with Topic – 2 team. You will need information from all those sensors.

## Slide 6: Topic - 4
Lane detection and following
  Detect lane markings and keep the car in between them
    Send commands to vehicle management controller accordingly
  Detect a cross road
    Execute a script for turning
You will get a new image and a board with LCD and a camera.
  Basic functions will also be provided for reading camera and displaying the image on the LCD.

## Slide 7: Topic - 5
Cool (read crazy) demonstrators
  Be creative!
  Use sensors and actuators cleverly
Begin with DE0 board and use the .SOPCINFO file provided last week
  Let us discuss what are your ideas we can then define strategy

## Slide 8: Topic - 6
Mobile App development
  Display sensor values in graphical way
  Display camera output
  Build navigational map and load it in the car
  Manual driving mode
  *Communication protocol*
Begin with your mobile phone
  Let us discuss some ideas
    How to display the sensor information in a catchy way
    Camera image
    RC-mode